## Slide 1: Adaptive Averaging of Non-Identical Image Series in the Wavelet Space
#3721
marschner@cbs.mpg.de
Henrik Marschner, André Pampel, & Harald E. Möller
Max Planck Institute for Human Cognitive and Brain Sciences, Leipzig, Germany
Adaptive Wavelet-based Enhancement of Signal Over Multiple Experiments (AWESOME)
ms
32 Element Head Coil
Body Coil
Body Coil + AWESOME
maps
8
Computer

## Slide 2: Overview: Adaptive Wavelet-based Enhancement of Signal Over Multiple Experiments (AWESOME)
Goal: Developing a Method for de-noising of MRI images of multiple measurements that does not alter quantitative information.
Idea: Utilizing the multitude of available images in several experiments (e.g. qMTI) to perform complex averaging by co-adding the different images. Shifting the complex averaging into the wavelet space to preserve experimentally controlled changes in the signals over the images.

## Slide 3: Background: Discrete Wavelet Transformation (DWT)
[2] By Alessio Damato (Own work) [GFDL (http://www.gnu.org/copyleft/fdl.html), CC-BY-SA-3.0 (http://creativecommons.org/licenses/by-sa/3.0/) or CC BY-SA 2.5-2.0-1.0 (http://creativecommons.org/licenses/by-sa/2.5-2.0-1.0)], via Wikimedia Commons
DWT
[1] By Andreas Tille, cropped by Alessio Damato (Image:Lichtenstein.jpg) [GFDL (http://www.gnu.org/copyleft/fdl.html) or CC-BY-SA-3.0 (http://creativecommons.org/licenses/by-sa/3.0/)], via Wikimedia Commons

## Slide 4: Background: Discrete Wavelet Transformation (DWT)
[2] By Alessio Damato (Own work) [GFDL (http://www.gnu.org/copyleft/fdl.html), CC-BY-SA-3.0 (http://creativecommons.org/licenses/by-sa/3.0/) or CC BY-SA 2.5-2.0-1.0 (http://creativecommons.org/licenses/by-sa/2.5-2.0-1.0)], via Wikimedia Commons
Level 1
Level 2



Multiple Scales or Level
Multiple Sub-bands or Directions of Analysis



and

## Slide 5: Background: Discrete Wavelet Transformation (DWT)
Exploited properties of DWT in the presented application:
Preservation of signal phase from MR images in their Wavelet-Representation [3]
Enhanced separation of “brain” and background noise via use of multiple scales and analysis directions [4]
[3] Olsen et.al., Wavelet Applications II, Pts 1 and 2, (1995). [4] Weaver et.al., Magn Reson Med, (1991).

## Slide 6: Background: MR Signal Properties
Exploited properties of MR signals in the presented application:
Predictability of signal phase enables phase corrections to achieve phase coherence of MR images across an image series
Knowledge on differences in distribution of MR data allow for characterization of data, e.g. into noise and meaningful signals in image and wavelet space likewise
[5] Dekker, A.J. den; Sijbers, J.; Phys. Med. (2014)

## Slide 7: Purpose of this Work
Combining advantages from two common approaches:
  Averaging via repetitions: “lossless” SNR improvement
  Wavelet de-noising via thresholding: Enhanced separation/characterization of data into noise or meaningful information in the wavelet space

## Slide 8: Purpose of this Work
Avoiding disadvantages of two common approaches:
  Averaging via repetitions: Necessity for repetitions of experiments under identical conditions
  Wavelet de-noising via thresholding: Loss of small meaningful information hidden in the noise background.

## Slide 9: Application Example: Pulsed MT Imaging
Experiment on a post mortem marmoset @ 3T (Bruker MedSpec 30/100); CP transceiver coil.[6]
3D MT-prepared GRE acquisitions (38 combinations from 11 off-resonance frequencies, 0.25-50 kHz; 7 MT pulse amplitudes, 0.6-7068 rad/s; NA=6-16);
map to correct off-resonance frequencies in the MT parameter estimation.
map.
Quantitative analysis for determining MT parameters. [7]
[6] R. Müller, Proc. ISMRM 21:4366, 2013. [7] D.K. Müller, A. Pampel, H.E. Möller. J. Magn. Reson. 230: 88 (2013).

## Slide 10: AWESOME: Step 1 - Input
Multiple images comprising magnitude and phase information
Axial slices of 3 selected images of the 38 image qMTI application example; Magnitude (top) and Phase (bottom) are shown

## Slide 11: AWESOME: Step 2 – Registration and Phase Correction
Registration of images may be performed if necessary
Phase correction includes correction of differences in phase over the series as well as removal of an average phase map
Application example only required phase correction due to non-moving post-mortem subject
Phase Correction

## Slide 12: AWESOME: Step 3 – Signal Phase Analysis
Determining characteristics of signal phase for a ROI of voxels over the series identified as meaningful (brain tissue) – e.g. standard deviation
Enable phase as identifier for noise/meaningful data
Application example shows a standard deviation of phase for meaningful data of
Phase Analysis

## Slide 13: AWESOME: Step 4 – Modeling 2D Classifier/Filter Function (Transfer Function)
Application example shows a standard deviation of phase for meaningful data of
Modeling a 2D classifier/filter function based on phase and intensity of an input value
Using any sigmoid function as modeling basis
Phase Filter

## Slide 14: AWESOME: Step 4 – Modeling 2D Classifier/Filter Function (Transfer Function)
Example phase filter part of the 2D Transfer Function; modeling basis is a logistic function
The passband width of the phase filter part is chosen to be wide enough to cover data of a phase close to the meaningful data phase
A width between and is chosen for “simple” Transfer Functions
Stopband
Passband

## Slide 15: AWESOME: Step 4 – Modeling 2D Classifier/Filter Function (Transfer Function)
Stopband
Passband
Example phase filter part of the 2D Transfer Function; modeling basis is a logistic function
The phase of data in the wavelet space can differ by 180°
Because of signs of local magnitude gradients in the image space and their effect on the wavelet transform

## Slide 16: AWESOME: Step 4 – Modeling 2D Classifier/Filter Function (Transfer Function)
Example phase filter part of the 2D Transfer Function; modeling basis is a logistic function
An extra passband around 180°is therefore necessary for correct data classification in the wavelet space
Stopband
Passband

## Slide 17: AWESOME: Step 4 – Modeling 2D Classifier/Filter Function (Transfer Function)
Example intensity filter part of the 2D Transfer Function; modeling basis is a logistic function
Intensity filter is modeled like-wise
The filter range is with a stopband to cover at least the interval to classify low intensity data as noise
Data will be normalized by standard deviation of noise
Combining Intensity and Phase Filter

## Slide 18: AWESOME: Step 4 – Modeling 2D Classifier/Filter Function (Transfer Function)
Product of Phase and Intensity Filter  2D Transfer Function TF
The filter function can be refined

## Slide 19: AWESOME: Step 5 – Wavelet Decomposition
Wavelet decomposition into level for good initial separation of noise and other data
“sym8” chosen

## Slide 20: AWESOME: Step 5 – Wavelet Decomposition
Complex wavelet decomposition; 3 of 7 Sub-bands from Level 1 and 2 of 5 for example image
Magnitude
Phase
Complex DWT
Real wavelet coefficients
Imag. wavelet coefficients
Level 3-5
Level 3-5
Wavelet-Representation

## Slide 21: AWESOME: Step 5 – Wavelet Decomposition
Note: Wavelet coefficients of meaningful data (brain) show a phase close to 0°or 180° as intended by the initial phase correction
Real
Level 3-5

## Slide 22: AWESOME: Step 5 – Wavelet Decomposition
Complex wavelet decomposition; 3 Example images and wavelet-representations
…
Averaging complex

## Slide 23: AWESOME: Step 6 – Averaging Wavelet-Representations
Level 3-5
Level 3-5
Wavelet-representation of first example image from series (left) Average wavelet-representation (right);
Averaging (complex)
Real
Real

## Slide 24: AWESOME: Step 7a – Analysis of Wavelet-Representations
Calculating phase difference for all coefficients of wavelet-representations of image series to corresponding coefficients of average wavelet-representation
is used in the classification of coefficients into noise and meaningful data
The phase difference of each coefficient is used as phase input for the Transfer Function

## Slide 25: AWESOME: Step 7b – Analysis of Wavelet-Representations
Analyzing coefficient intensity distribution for each wavelet-representation (WR)
Calculating the standard deviation of the central peak (see histogram, right) for each WR -
Intensity analysis

## Slide 26: AWESOME: Step 7b – Analysis of Wavelet-Representations
Calculating normalized WR
Magnitude of normalized wavelet-representations is used as intensity input for the Transfer Function
Intensity analysis

## Slide 27: AWESOME: Step 8 – Applying Transfer Function
Using and for each coefficient and wavelet-representation of images of the series for deriving a Transfer Function for classifying each coefficient into noise and meaningful data

## Slide 28: AWESOME: Step 8 – Applying Transfer Function
Level 3-5

## Slide 29: AWESOME: Step 9 – Calculating Scaling Factors
The average coefficients have a reduced noise contribution
Averaged coefficients are computed to substitute the original coefficients
Meaningful contributions in average and original coefficients are assumed to be phase coherent
A possible measure of phase coherence is

## Slide 30: AWESOME: Step 9 – Calculating Scaling Factors
Using phase coherence property to calculate the sum of meaningful contributions (S) from original coefficients.
magnitude of normalized wavelet-representations phase difference of original and average wavelet-representations.

## Slide 31: AWESOME: Step 9 – Calculating Scaling Factors
Scaling factor C is calculated from the ratio of and S scaled by
Scales average coefficient to meaningful part of original coefficient.

## Slide 32: AWESOME: Step 10 – Calculating De-Noised Wavelet-Representations
Calculation aims to replace noisy coefficients in original wavelet-representations
Coefficients are classified as noise and meaningful data by Transfer Function
Average coefficients with better SNR are used in replacement
Average coefficients are scaled by scaling factors to have magnitude of possible meaningful parts in original coefficients

## Slide 33: AWESOME: Step 10 – Calculating De-Noised Wavelet-Representations
where are the values of the applied transfer function, are the original wavelet-representations, is the average wavelet-representation, and are the rescaling factors.

## Slide 34: AWESOME: Step 10 – Calculating De-Noised Wavelet-Representations
Wavelet-representations of all images from the series are de-noised via AWESOME pipeline
Using unique transfer function values and rescaling factors for each image’s wavelet-representation in the pipeline

## Slide 35: AWESOME: Step 10 – Calculating De-Noised Wavelet-Representations
Original
De-noised
Real wavelet coefficients
Level 3-5
Real wavelet coefficients
Level 3-5

## Slide 36: AWESOME: Step 11 – Wavelet Reconstruction and Post-Processing
Wavelet Reconstruction of de-noised wavelet-representations for each image
Optional: Reverse phase correction

## Slide 37: AWESOME: Step 11 – Wavelet Reconstruction and Post-Processing
Original
AWESOME
Magnitude

## Slide 38: AWESOME: Optional Modifications
Modifications to the transfer function and/or the scaling factor calculation can be helpful if false positive classifications of noise as meaningful data occurs in the wavelet-representations
Misclassification is caused, e.g., by spurious signals due to insufficient spoiling
Spurious signals lead to partial correlation of noise  phase coherence similar to meaningful data

## Slide 39: AWESOME: Optional Modifications
Phase coherence can be observed in the phase images of the original data
Gaussian Noise (e.g. random phase distribution)
Non-Gaussian Noise (e.g. patterned phase distribution)

## Slide 40: AWESOME: Optional Modifications
Optional transfer function modification are:
  Reductions in phase filter width for an intensity range higher than , depending on the spurious signal strength
  An extension of the stopband in the intensity filter to higher intensity likewise

## Slide 41: AWESOME: Optional Modifications
Example „modified“ 2D Transfer Function; narrow phase filter for intensities <7
Broader phase filter widths above observed noisy coefficient intensities are optionally allowed
Phase coherence based risk of false positive classifications vanishes due to intensity limit of noise

## Slide 42: AWESOME: Optional Modifications
Optional scaling factor calculation modification are:
  Choice of different measure of phase coherence than
  Implementation of scaling factors derived from combined phase and intensity based probability distributions of noise and meaningful data in the wavelet space

## Slide 43: AWESOME: Results qMTI
[6] R. Müller, Proc. ISMRM 21:4366, 2013.
Experiment:
1 post-mortem marmoset brain
3T (MedSpec 30/100, Bruker, Ettlingen, Germany)
(0.2mm)3 isotropic resolution
Signal reception with CP transceiver coil [6]

## Slide 44: AWESOME: Results qMTI
[7] D.K. Müller, A. Pampel, H.E. Möller. J. Magn. Reson. 230: 88 (2013).
Experiment:
3D MT-prepared GRE acquisitions (38 combinations from 11 off-resonance frequencies, 0.25-50 kHz; 7 MT pulse amplitudes, 0.6-7068 rad/s; NExp=6-16)
map to correct off-resonance frequencies in the MT parameter estimation
map
Quantitative analysis for determining MT parameters [7]

## Slide 45: AWESOME: Results qMTI
Results are shown for the presented pipeline of AWESOME
Results from measurements that were repeated up to 16x for classical averaging are used as reference
Additional results are shown for a modified AWESOME pipeline with above introduced modification of the transfer function
AWESOME modified using reference as optimum

## Slide 46: AWESOME: Results qMTI
Non-Gaussian noise in the application example is observed for images of high signal intensity
Gaussian noise is observed for images of low signal intensity
Phase maps of example images
Gaussian Noise (e.g. random phase distribution)
Non-Gaussian Noise (e.g. patterned phase distribution)

## Slide 47: AWESOME: Results qMTI
Comparison of Magnitude Images
Shown images are 3 examples of a series of 38 different images
For better visual comparison a gray scale representation is shown

## Slide 48: AWESOME: Results qMTI
Original
Averaged, Nexp=
6x
6x
9x
AWESOME
AWESOME, modified

## Slide 49: AWESOME: Results qMTI
Original
Averaged, Nexp=
6x
6x
9x
AWESOME
AWESOME, modified
De-noising without noticeable blurring
Preservation of unique contrast and intensity features for different images

## Slide 50: AWESOME: Results qMTI
Comparing non-averaged (low SNR, raw), AWESOME (awe) improved, and modified AWESOME (awemod) improved with averaging-via-repetition (high SNR, ref) improved images In of the series:
Calculating all following values for a mask, covering only brain tissue

## Slide 51: AWESOME: Results qMTI
Comparing non-averaged (low SNR, raw), AWESOME (awe) improved, and modified AWESOME (awemod) improved with averaging-via-repetition (high SNR, ref) improved images In of the series:
Calculation of the sum squared difference over n=1:N images

## Slide 52: AWESOME: Results qMTI
Comparing non-averaged (low SNR, raw), AWESOME (awe) improved, and modified AWESOME (awemod) improved with averaging-via-repetition (high SNR, ref) improved images In of the series:
Calculation of Spearman’s rank correlation coefficient
Fit of parameters of a binary-spin-bath model (described in detail in [7]) to a pair of random chosen white and gray matter voxels; Calculating the norm of the residual as quality measure of fit
[7] D.K. Müller, A. Pampel, H.E. Möller. J. Magn. Reson. 230: 88 (2013).

## Slide 53: AWESOME: Results qMTI
Graphic shows SSDs of equal scale for following 3 cases: A: SSD of unmodified AWESOME (Gaussian noise) B: SSD of modified AWESOME (non-Gaussian noise) C: SSD of non-averaged series
A
B
C
Sum Squared Difference

## Slide 54: AWESOME: Results qMTI
Graphic shows M0b for equal scale and the following 4 cases: A: Reference series B: Modified AWESOME (non-Gaussian noise) C: Unmodified AWESOME (Gaussian noise) D: Non-averaged series
A
B
C
qMT parameter example – M0b relative size of semi-solid pool
D

## Slide 55: AWESOME: Results qMTI
 | Average * | Spearman’s ρ | Norm of the residuals* | 
 |  |  | Gray matter | White matter
High-SNR reference | — | — | 0.778 | 0.453
Low-SNR data | 1 | 0.985 | 1 | 1
‘Standard AWESOME’ | 0.651 | 0.991 | 0.773 | 0.651
‘Modified AWESOME’ | 0.477 | 0.994 | 0.773 | 0.474
 |  | Spearman’s ρ | Norm of the residuals* | 
 |  |  | Gray matter | White matter
High-SNR reference | — | — | 0.778 | 0.453
Low-SNR data | 1 | 0.985 | 1 | 1
‘Standard AWESOME’ | 0.651 | 0.991 | 0.773 | 0.651
‘Modified AWESOME’ | 0.477 | 0.994 | 0.773 | 0.474
*Values normalized to the result from the low-SNR data without averaging and de-noising

## Slide 56: AWESOME: Results T2
Experiment:
1 young, healthy adult with no known abnormality
3T (Verio, Siemens Healthcare, Erlangen, Germany)
(1mm)3 isotropic resolution
Signal reception with Body Coil (BC) and 32-element Head Coil as reference
Commercial Spin-Echo MRI sequence, , 32 Echoes with full k-space sampling

## Slide 57: AWESOME: Results T2
AWESOME for Gaussian noise (no modifications) is applied
Noise reduction is consistent over all echoes
BC
BC-AWESOME
REF

## Slide 58: AWESOME: Results T2
Estimated maps are subtracted from Head Coil reference for maps
Gray scale image, the first echo from the Head Coil
ms
32 Element Head Coil
Body Coil
Body Coil + AWESOME
maps
maps

## Slide 59: AWESOME: Results T2
Spin-Echo Decay of a single WM voxel
32-Ch-Head Coil
Body Coil noise  single exponential fits differ from reference
Body Coil + AWESOME  fits almost identical compared to reference
TE / ms
Normalized Signal Intensity
Fits only

## Slide 60: Conclusion
AWESOME effectively reduces noise, as visible in the reduced SSDs
Main features, that need no improvement, stay untouched by exclusion from averaging via the transfer function
Hidden features are restored via approximation of rescaling factors, as observed in the increased correlation coefficient and improved fit error

## Slide 61: Conclusion
AWESOME for Gaussian noise delivers good results also for partially non-Gaussian noise. The presented pipeline can be used as a basis version for application and modification.
Modifications to AWESOME for non-Gaussian noise may be performed individually…

## Slide 62: Outlook
AWESOME should be investigated on experiments of repetitive imaging:
qMTI and CEST (in progress)
fMRI, where imaging of the brain is repetitively performed
Other experiment, in which image data are repetitively recorded as a function of time, e.g., in perfusion imaging with ASL or DSC techniques, blood volume mapping by VASO, …

## Slide 63
Thank you for your interest!
Acknowledgements:
Funded by the Helmholtz Alliance ICEMED—Imaging and Curing Environmental Metabolic Diseases.